| Command | Command Alias | Icon | Menu | Result |
| --- | --- | --- | --- | --- |
| Array | AR |  | Modify ( Array | Creates a rectangular or circular pattern of the selected objects. |
| Chamfer | CHA (A or D) |  | Modify ( Chamfer | Creates an angled corner between two lines. |
| Circle | C |  | Draw ( Circle ( Center, Radius | Draws a circle based on a center point and radius. |
| Copy | CP (Or CO) |  | Modify ( Copy | Copies object(s) once or multiple times. |
| Dimension | Dim | Many | Annotate ( (pick one) | Dimensions previously drawn objects |
| Erase | E (Or the delete key) |  | Modify ( Erase | Erases an object. |
| Extend | EX (Enter twice) |  | Modify ( Extend | Extends objects to a selected boundary edge. |
| Fillet | F |  | Modify ( Fillet | Creates a round corner between two lines. |
| Layer | LA |  | Layer ( Layer | Starts the Layer and Linetype property dialog box. |
| Line | L |  | Draw ( Line | Draw a straight line from one point to the next |
| Mirror | MI |  | Modify ( Mirror | Creates a mirror image of an object or selection set. |
| Move | M |  | Modify ( Move | Moves an object or objects. |
| Multiline | ML |  | Draw ( Multiline | Draw two or more parallel lines based on the parameters you define. |
| Object Snaps | OSNAP | RIGHTCLICK | Icon at Bottom ( Object Snap Settings… | Brings up the OSNAP dialog box. |
| Offset | OF |  | Modify ( Offset | Offsets an object (parallel) by a set distance. |
| Print | PRINT (Or PLOT) |  | File ( Print | Enables the Print/Plot Configuration Dialog Box |
| Rectangle | REC |  | Draw ( Rectangle | Draws a rectangle after you enter one corner and then the second. |
| Rotate | RO |  | Modify ( Rotate | Rotates objects to a certain angle |
| Scale | SC |  | Modify ( Scale | Proportionately enlarges or shrinks (scales) objects. |
| Stretch | S |  | Modify ( Stretch | Stretches an entity after you have selected a portion of it. |
| Text | TEXT, DTEXT, MTEXT | None | Draw ( Text Single Line Text or Multiple lines | Creates a line of text |
| Trim | TR (Enter twice) |  | Modify ( Trim | Trims objects to a selected cutting edge. |