AutoCAD FLOOR PLAN INSTRUCTIONS

A

Open: PPLAN1 on S Drive

Save As: Floor Plan with Dimensions A

Use PLINE to draw all exterior walls using flplan layer (walls should be blue)

You must use the ‘ mark at the end of the number for feet.  To input feet and inches and fractions of an inch, use 34’ 2-1/2”.

OFFSET 5 ½” to the inside to give the thickness of the walls

EXPLODE all walls

OFFSET using dimension given to locate the center of all interior walls

DIMENSION given dimensions using dimension layer (Approximate Measurements: First Dimension line 4’ – 0” from object line, Second Dimension line     1’ – 6” from first dimension line)

Add TEXT for room names in ALL CAPS using the dimension layer.  Change text height to 1’ (Use ROTATE as needed)

INSERT title block by browsing for UGHS ARCHITECTURAL TITLE BLOCK

Place title block on drawing.  Title block should be in detail layer.

EXPLODE title block.

Double click to change TEXT: Last Name Floor Plan, Your Name House and the Date.

Add the letter A onto your title block where it says FPI change it to FPA.

PRINT: Select window for what to plot and check center the plot

B

Open: Floor Plan with Dimensions A

Save As: Floor Plan with Dimensions B

OFFSET 1¾” on each side of all interior walls to get a 3½” wall.  Be sure to ZOOM in to offset to both sides of the center.

Delete the centerline of each wall

Use FILLET and TRIM to clean up wall corners and intersections

Add the letter B onto your title block where it says FPI change it to FPB.

PRINT: Select window for what to plot and check center the plot

C

Open: Floor Plan with Dimensions B

Save As: Floor Plan with Dimensions C

INSERT all doors and windows to given dimensions.  If a dimension is not given, assume it is in the center of interior walls if it looks centered, otherwise, for interior doors, hover over the closest intersection and move cursor in the direction of door and type 6.  The door will input 3” from the intersection.

**When in the insert box, check specify on-screen under the rotation section in order to more easily rotate doors and windows

Use the plan given (in front of Floor Plan C) to locate door and window placement and type (door 1 is the same as door 22)

Use COPY, ROTATE and MOVE

For doors on an exterior wall, it may be necessary to place door, EXPLODE door, and then LENGTHEN cyan lines to extend the full 5-1/2” thickness for exterior wall.

Add the letter C onto your title block where it says FPI change it to FPC.

Do NOT Print

D

Open: Floor Plan with Dimensions C

Save As: Floor Plan with Dimensions D

Finish adding all exterior and interior dimensions (Approximate Measurements: First Dimension line 4’ – 0” from object line, Second Dimension line 1’ – 6” from first dimension line, Third Dimension line 1’-6” from second dimension line, Fourth Dimension line 1’-6” from third dimension line)

Add the letter D onto your title block where it says FPI change it to FPD.

PRINT: Select window for what to plot and check center the plot

E

Open: Floor Plan with Dimensions D

Save As: Floor Plan with Dimensions E

INSERT fixtures and appliances using given plan on previous page

Draw interior wall in second bath after inserting bathtub

Use furniture layer to draw closet rods.  Closet rods are located by drawing a line from midpoint to midpoint on the interior of each closet.

Use outline layer to draw cabinets and closet shelves.  Closet shelves will be offset 1” towards the door side of closet from the rod.

Move room names to avoid conflicts if possible

Add the letter E onto your title block where it says FPI change it to FPE.

PRINT: Select window for what to plot and check center the plot

F - BONUS

Open: Floor Plan with Dimensions E

Save As: Floor Plan with Furniture

Delete all dimensions and INSERT fixtures and furniture using given plan (approximate placement is acceptable)

Add the letter F onto your title block where it says FPI change it to FPF.

PRINT: Select window for what to plot and check center the plot